## Slide 1: GUM OPTIMISATION Overview
September 2022

## Slide 2: OVERVIEW
In December ‘21, we ran a “Value Discovery Lite” consisting of 2 workshops to ascertain the desirability, scalability and feasibility of the use cases
WORKSHOP #1
E
WORKSHOP #2
VALUE DISCOVERY ACTIVITIES DURING MVP
Objectives:
  Determine value to be targeted with use case at Gainesville and potential scalability
Activities:
  Working session to model potential savings based on site data (use case dependent – use case shared in advance as per pre-requisite)
Attendees:
  Process owners at site
  Site finance
  Process lead in other relevant regions
Objectives:
  Detail use case to enough granularity to allow MVP scoping
Activities:
  Define manufacturing process to be targeted - Process mapping as is and to be
  Identify intervention points that the solution will use
  Determine data sources and complexity of integration
  Overlay key opportunity areas, value drivers and data sources
Attendees:
  Process owner at site
  Technical Lead at site
VALUE DISCOVERY “LITE” ACTIVITIES
Detailed As-Is and To-Be Journey Mapping
Value Validation and Expected Realisation
Roadmap for roll-out and associated benefits
Detailed user requirements for build

## Slide 3: Potential use cases
BATCH MANAGEMENT
GUM MEASUREMENTS
GUM DEFECTS
1
2
3
Automated batch reporting system for visibility of unknown issues resulting in higher quality and more consistent gum.
Use visual inspection to measure circular LAND settings that eliminates operator subjectivity to improve the regularity of gum measurements, score depths and reduce short stops downstream in the wrapping process.
Use visual inspection to identify holes/spots & trim abnormalities to improve gum quality and reduce short stops further downstream in the wrapping process.
Out of scope
YRV
YRV + GNV
We arrived at three potential use cases that could be applicable to Yorkville and Gainesville and decided to take two of these forward into MVP.

## Slide 4: SOLUTION OVERVIEW

## Slide 5: Gum Measurement YRV Solution Overview
Cooling & Packaging
The Challenge: To eliminate regularity of gum parameters to reduce short stops further downstream in the wrapping process. The aim is to alert operators when gum measurements are out of a defined threshold and make adjustments based on the level of error, to create product in spec.
3 Sizing Rollers applied to sheet before scoring (thickness
Circular Scoring Rollers (x26)
Cross-Scoring Rollers (x6)
Last Roller
LTO
Line Scan Camera + Strobe Light
Camera measuring length of gum sticks through image capture.
Images processed by respective Keyence software on device’s controller.
X = length of gum stick (2.86in)
Y = width of gum stick (0.74in)
Each card consists of 26 sticks
Card dimensions = 19.3in by 2.8in
Moving Belt Direction
Cold Scoring Line
Laser Profiler
Laser continuously measuring width and land score depth of gum sticks
Images processed by respective Keyence software on device’s controller.
Rotational encoder to synchronise camera shutter with belt movement.
1
1
2
The laser profiler continuously measures the width of the gum sticks as well as circular land score depth. The camera is placed after the Circular Scoring Rollers above and centre of the cards.
Scanning Area = 39mm (2 Circular Land Scores)
Width : Distance between score lines
Depth: Roller balance and knife + scraper settings
Roller Balance, Scraper and Knife Position (x25)
2
The line scanner is placed above and perpendicular to the moving belt. The camera’s shutter is synchronized to the belt movement by using a rotational encoder. When a signal from the encoder is received, the camera takes a picture.
A strobe light illuminates the back of the cards.
3
3
The line scanner take a series of line images and combines these to form a 3 x 2” ‘Field of View’.
Power BI Dashboard Analytics
Real-Time
Users are able to see if the length, width and land score depth of the gum stick is within a maximum and minimum threshold across a 30 minute time period.
Users can view the total number of errors above or below threshold of each type of measurement within a 30 minute time period.
Predictive
Users can see if a measurement will be above or below threshold in the next 20 minutes.
Historic
Users can view the average length, width and land score depth across a selected shift or SKU. They can also drill down into the total number of errors in each run as well the median of the hours during which an error has occurred.
Alerts
An alert is provided when gum measurements are +/- their ideal threshold. Users can accept and reject these alerts. A reject indicates that the operator believes an error is not significant. Chosen actions are displayed on the dashboard. Alerts are considered expired after 15 mins.

## Slide 6: Gum Defects GNV Solution Overview
Cooling & Packaging
The Challenge: To identify holes/spots & trim abnormalities to improve regularity of gum parameters and prevent short stops downstream in the wrapping process. The aim is to identify which sheets have defects so that they can be removed before reaching the packaging area and causing delays.
3 Sizing Rollers applied to sheet before scoring (thickness)
Circular Scoring Rollers (x26)
Cross-Scoring Rollers (x6)
Last Roller
LTO
Camera 1: Area Camera
Captures image of whole gum sheet area
Camera 2: Line Scan Camera
Camera builds 2D image which displays identifiable defects
Images processed by respective software on device’s controller.
Sheet = 26x6 gum sticks
130 Sheets/minute produced
Moving Belt Direction
Traditional Line
2
2
The cameras are placed after the last roller with an additional light source.
The camera’s shutter speed will be synchronised with the belt’s movement to capture a single sheet of gum. The camera will capture 130 images per minute.
ID of Load Production,
Current Shift
The solution will aim to detect the following defects:
Holes
Ingredient Spots
Ragged Edges
and match these to the production run so that individual defected sheets can be identified.
1
Laser Trigger Model TBD
1
3
The machine learning model for automatic defect detection is to be determined depending on accuracy, complexity and time to train the model.
The model will aim to count the number of good sheets produced and identify the number of defects as they arise.
With time, a Power BI dashboard will be able to alert operators of gum defects before they enter packaging and reduce detection time by up to 2-3 days.
4

## Slide 7: MVP VALUE CASE

## Slide 8: Gum Optimisation Value Case - GNV
Non Quality Cost Avoidance
$86,203
Downtime Cost Avoidance
$324,272
Capacity
$383,500
TOTAL LOSS
$47,411
$178,350
$210,925
ADDRESSABLE LOSS
$436,686
Avoidance of edge trim waste and waste at the cutting and packaging process.
Avoidance of short stops and downtime in the packaging process.
Avoidance of short stops and downtime based on 80% utilisation rate at GNV
Gum Optimisation Value Case - YRV
Non Quality Cost Avoidance
$144,000
Downtime Cost Avoidance
$555,234
Capacity
TBC
TOTAL LOSS
$79,200
$305,378
TBC
ADDRESSABLE LOSS
Avoidance of edge trim waste and waste at the cutting and packaging process.
Avoidance of short stops and downtime in the packaging process.
Avoidance of short stops and downtime
ASSUMPTIONS ARE FROM ORIGINAL VALUE CASE AND HAVE NOT BEEN VALIDATED IN COMPARISON TO THE EXISTING SOLUTION AS IT IS NOT CURRENTLY LIVE.
$384,578